## Slide 1: Tactile Smoke-Detector Interface
David Burson
Supervised by Dr Barry McMullin
B. Eng Electronic Engineering 2013

## Slide 2: Project Brief
Fires are an added danger to people who are deaf/hard of hearing as they may fail to hear a smoke detector.
Design a solution that will provide a mobile, tactile danger warning to a user in the case of a smoke detection.
Tactile Smoke-Detector Interface

## Slide 3: Breakdown of Problems
Method of sensing a danger?
  Investigate common smoke detection methods.
  Choose one.
How to process danger?
  How to handle multiple detection points?
How to communicate danger to user?
  Develop portable device or adapt existing?
  How to handle multiple detectors in a location?
Tactile Smoke-Detector Interface

## Slide 4: Problem Solving
Method of sensing a danger
  The most common household fire detection method is a ceiling mounted smoke-detector.
  Operate in two ways; Ionization or Photoelectric
  Smoke Detectors’ IC can be adapted using designated
  I/O Pin to interface with a microcontroller.
Tactile Smoke-Detector Interface

## Slide 5: Problem Solving
How to Process Danger
  Select a microcontroller
  PIC or Arduino?
  Arduino UNO, compact & practical for early prototyping
  Multiple Analog, Digital and Power I/O Pins
  Serial Interface
Tactile Smoke-Detector Interface

## Slide 6: Problem Solving
How to Communicate Danger?
  How to handle multiple detectors in a home
    433 MHz RF Transmitter interfaced with microcontroller on each smoke-detector.
    RF Receiver at central ‘server’ receives signal and processed by microcontroller.
Tactile Smoke-Detector Interface

## Slide 7: Problem Solving
How to Alert Hearing-Impaired User?
  Mobile alert method
    A mobile phone is a ready-made portable device, danger alert can be achieved by sending a warning call or SMS.
    Incorporate a GSM module into the receiver circuit in order to transmit calls or SMS’.
    Chose the SIEMENS TC35 GSM Module Development Board.
Tactile Smoke-Detector Interface

## Slide 8: Problem Solving
How to Alert Sleeping User?
  Under pillow vibrator.
  When warning signal is received, vibration motor pulses in plastic encasement to wake sleeping user.
  If user chooses to keep phone by bedside, provides two alternating vibrating alerts.
Tactile Smoke-Detector Interface

## Slide 9: Progress
Smoke-Detection/Transmitter Circuit
  I/0 pin sends analog voltage signal to microcontroller when activated.
  Program detects high input, transmits RF signal.
  Test Push Button.
  Battery Powered.
Tactile Smoke-Detector Interface

## Slide 10: Progress
Receiver/Warning Circuit
  RF Receiver collects signal.
  Signal processed by microcontroller.
  Program sends AT commands to GSM module in order to transmit warning call or SMS.
Tactile Smoke-Detector Interface

## Slide 11: To Do
Develop code in order to remotely program the call-out number via SMS
  Proving difficult due to serial connection between TC35 and GSM Module.
Develop suitable and safe under-pillow vibrator.
Package project in user-friendly and aesthetically suitable way.
Tactile Smoke-Detector Interface

## Slide 12: Conclusion
Tactile Smoke-Detector Interface
Smoke detectors with a small and inexpensive pairing of a RF transmitter and microcontroller transmit a warning
Received via RF Receiver, processed by controller
Warning phone call is made via the GSM module to users mobile phone
Pillow shaker/vibrator is switched on in a pulse loop to wake a sleeping individual
I now invite questions from the audience.